# TABLE SAW RULES

# For your safety, the table saw should have a large shut-off button, a guard and a splitter in good working order.

# The blade and fence should be parallel to the slots in the saw tabletop.

An effective push stick should be on the saw within reach at all times.

Never clear away scraps or cut-offs when the saw is running!!

Rip wood less than 6”wide with a push stick.

10” minimum length of wood to be ripped.

Wood must have a straight edge against the rip fence!

Set the blade only 1/8” higher than wood.

Keep the fast lane OPEN by standing to the left of blade.

On wider pieces, control the fast lane.

Left hand never goes past blade.

Keep both hands 4” away from blade at all times!

Tuck your thumb into your palm when pushing with your hand.

Listen to the saw and respond to what you hear.

Push the wood all the way through the lane past the blade and then shut off the saw.

Never reach over the blade to support or retrieve wood!

In the event of a problem, hold wood and shut saw off with large push button with your knee.